ECL-1:

100 ml    0.1M Tris.Cl (pH 8.6)

60   ul     H2O2 (30%)

ECL-2:

100   ml     0.1M Tris.Cl (pH 8.6)

1       ml     Luminol (250 mM)

0.44  ml     P-Coumaric Acid (90 mM)

H2O2: SIGMA H-0904

Luminol: SIGMA A-8511   (250mM: 2.2g + 50 ml DMSO)

P-Coumaric Acid: SIGMA C-9008 (90mM: 0.75g + 50 ml DMSO).

Note: I store the solution in 4 degree in dark. They can last at least 2 months with no decrease in quality.